Table of Contents

1.	Setting-up your Windows computer and screen reader	5

1.1	Brailliant USB driver installation:	5

1.2	JAWS driver installation	8

2	Using Brailliant with Windows computers	10

2.1	Connecting via the USB port	10

2.2	Connecting your Brailliant via Bluetooth	10

3	Mac computers	12

3.1	Connecting via the USB client port	12

3.2	Connecting via Bluetooth	12

4	iPhone, iTouch and iPad iOS 5.1	13

4	System Access	17

5	NVDA	17

6	Using Brailliant's keys	18

7	Screen Reader Command summary	19

7.1	JAWS command summary	19

Basic Commands	19

PC keyboard emulation for Brailliant	21

7.2	Window-Eyes command summary	23

Window-Eyes basic commands	23

Modifier Keys	24

7.3	Apple iOS devices Command summary	25

Basic navigation commands	25

Reading commands	26

Information commands	26

Rotor commands	26

Edit commands	26

Miscellaneous commands	26

7.4	Mac command summary	27

Basic navigation commands	27

Reading commands	27

Information commands	27

Miscellaneous commands	27

7.5	Using your Brailliant with System Access	28

Braille Preferences	28

Braille Input with System Access	28

Braille Navigation Key reference Universal Keystrokes	29

7.6	NVDA command summary	29

8	Appendix	31

- Using Brailliant with Screen Readers

Did you know that you can run a screen reader (such as JAWS, Window-Eyes on your Windows computer or VoiceOver on your Mac)) using your Brailliant? You can also read and type information in Braille to your iPhone or iPad.

Brailliant offers flexible connectivity options. You can connect your Brailliant through the USB port. It also allows you to enjoy the freedom of wireless Bluetooth connectivity.

# Setting-up your Windows computer and screen reader

To set-up your computer, you will need to:

- Install the USB driver: Using USB client port requires the installation of a driver on your computer.

- Install the JAWS driver: If you are using JAWS, you will need to install the JAWS driver. If you are using other screen readers, the drivers are already included.

Note: Both drivers can be installed with Windows XP, Windows Vista (32 and 64 bits) and Windows 7 (32 and 64 bits) operating systems.

Both the Brailliant USB driver and the JAWS Brailliant driver are included in the Brailliant Companion CD. You can also download it from our Web site at: www.humanware.com/Brailliant_support.

## Brailliant USB driver installation:

Follow the instructions below to install the USB driver. Don't connect your Brailliant before installing the driver. Please note that these instructions apply for all Brailliant BI and B models.

- Download the BrailliantBITools.exe file on your PC. Note the location where you downloaded the file.

- Open the file BrailliantBITools.exe.

- Select Install Brailliant BI USB driver or press Alt-U to start the installation. This process will preinstall the driver files on your computer.

- By default, your Brailliant channel is set to Auto. When a USB cable is connected, the unit will work in USB mode.

- Connect the small end of the client USB cable into the micro USB port on the right edge of the Brailliant, just next to the Power button. Plug the standard USB end into a USB port on your PC.  You will hear a rising tone indicating that the PC has recognized the connection.

- You will be presented with a Device Driver Installation Wizard window. Select the NEXT button to continue.

- You may be presented with a warning stating that Windows cannot verify the publisher of this driver software. Simply select the "Install this driver software anyway" button.

- Select NEXT when the installation process has run its course.

- After installation has been completed, you will be presented with a completion message.  Select FINISH to conclude the installation.

If you want to use your Brailliant with Window-Eyes, you can Exit the Braille Terminal Tools immediately. The Window-Eyes Brailliant driver is available directly in Window-Eyes, starting with version 7.5.2.

## JAWS driver installation

Follow the instructions below to install the Brailliant driver for JAWS version 10 or later. Please note that these instructions apply for all Brailliant BI and B models.

- Open the file BrailliantBITools.exe

- Select Install Brailliant BI driver for JAWS version 10 or later, or press Alt-J to start the installation.

- A window will appear to inform you that installation will begin shortly.

- To begin installation select NEXT.

- Select INSTALL to start the JAWS driver installation.

- Select YES to use your Brailliant as your default Braille display.

- Select FINISH to conclude the installation process.

- If your JAWS is already running, close it and restart it for changes to take effect.

# Using Brailliant with Windows computers

## Connecting via the USB port

Once the USB driver is installed, simply connect your Brailliant to your computer using the USB cable. The Brailliant will automatically recognize the connection.

## Connecting your Brailliant via Bluetooth

To use the Brailliant with a screen reader via Bluetooth, you will first need to add the Brailliant as a Braille display within your screen reader.

On the Brailliant

By default, your Brailliant channel is set to Auto.

If there is no USB cable connected, the Bluetooth channel communication will be activated.

On the PC

Perform a Bluetooth search. When the Brailliant is displayed in the list of Bluetooth devices, select the Brailliant from the list. When prompted for an authentication code, type the code "1111", and then confirm this.

The device should then pair with the Brailliant and an incoming Bluetooth virtual serial port will be set up on the PC.

You should now check the Properties of the Brailliant connection in your Bluetooth Manager to find out which COM port number has been assigned to the incoming Bluetooth serial port.

Make a note of this number. On the PC, in your screen reader, set the active braille display COM port to use as the relevant Bluetooth serial port COM number.

If using JAWS, you will need to quit and restart it.

# Mac computers

## Connecting via the USB client port

- Simply connect your Brailliant to your computer using the USB cable. The Brailliant will automatically recognize the connection.

- Insert the larger end of the cable into one of the Mac's USB ports. If the Brailliant does not display the item on the Mac, then switch the Brailliant off and on. Items from the Mac should then be displayed on the Brailliant.

## Connecting via Bluetooth

To establish the connection, do the following:

- Before attempting to pair the Apex with the Mac, you will need to ensure that Bluetooth has been turned on for the MAC and that it is discoverable by other devices.
From the Mac's desktop, open the menu bar; move the VO cursor down through the menu and select System preferences.  Interact with the scroll area of the Preference panes.  Move to the Bluetooth button and press it.  Make sure that the check box for Bluetooth on as well as the box for discoverable are both checked.  Then, close the Window.

- On the Brailliant, make sure the channel is set to Auto and no USB cable is connected. Set the channel to Bluetooth if a USB cable is connected.

On your MAC, from the desktop:

- Open Voiceover Utilities by pressing the VO keys with F8.  Interact with the table of categories and move to Braille.

- Stop interacting with the table and move the VO cursor to the Displays tab and press the VO keys with Space to activate that tab.

- Move the VO cursor to the right until you find the "Add Braille Display" button and select it. The Mac will search for Bluetooth Braille displays.

- When you hear that the Mac has found a display, move the VO cursor to the right to the table of discovered displays and interact with the table. Move the VO cursor down and find the Brailliant.

- Stop interacting with the table.

- When you no longer hear “busy” from the progress bar, move the VO cursor to the right, find the “select” button and activate it.

- A pairing request Window will appear, accept it by pressing Enter to complete the pairing process.

- If the pairing is successful, the Brailliant will display the contents of the VO cursor.

# iPhone, iTouch and iPad iOS 5.1

The Brailliant BI can be paired with iOS devices running iOS 5.1 as a Bluetooth Braille display and provides Grade 2 braille input and output.

The pairing has to be initialized from the iOS device, just as you would to pair with any other keyboard or Bluetooth device.

To make the connection do the following:

From the Brailliant menu, make sure to select Auto or Bluetooth as the communication channel

| 1. Tap on the settings application from the Home screen. | 2. Tap on "General." |
| --- | --- |

| 3. Towards the bottom of the screen tap Accessibility. | 4. Tap on VoiceOver. Make sure it is enabled. |
| --- | --- |

| 5. Double Tap on Braille. | 6. If Bluetooth is not enabled Double tap "Yes," to enable it. |
| --- | --- |

| 7. Double Tap the Brailliant when displayed in the list. | 8. Double tap on the “Pair” button to confirm pairing. The PIN code won’t appear on your Braille display. |
| --- | --- |

9. The Brailliant will now show as paired in the list of braille devices and the IOS device can now be controlled by the Brailliant's input keyboard.  The Brailliant's braille display will represent in braille everything that is spoken by the VoiceOver screen reader.  Note that if the IOS device is locked, pressing the Home button on the IOS device will unlock the device and the Brailliant will automatically reconnect to it as a braille device.

Apple iOS devices Command Summary

# System Access

Using your Brailliant display with System Access is easy and seamless. Best of all, you can use your Brailliant with System Access on your home computer as well as any other computer you may encounter in the field. No driver installation is required, you need only to connect your Brailliant display in to an available USB port or pair it to a computer via Bluetooth, and you'll have accessibility anywhere, right at your fingertips.

After connecting your Brailliant using USB or Bluetooth, you are ready to begin using it with System Access. If System Access is already running, close the program with Modifier+F4 and launch it again with Control+Alt+S if running from your installed copy, or by running www.satogo.com if using through System Access to Go. When System Access launches, it will automatically detect your display and you'll immediately receive Braille output.

Command Summary for System Access

# NVDA

You can use your Brailliant with the free screen reader NVDA (NonVisual Desktop Access). The software is available for download at: http://www.nvda-project.org/wiki/Download

Before launching NVDA, make sure to connect your Brailliant using USB or Bluetooth. If you have installed NVDA with the installer, then starting NVDA is as simple as either pressing control+alt+n, or choosing NVDA from the NVDA menu under Programs on the Start Menu. Additionally you can type NVDA into the Run dialog and press Enter. To start the portable version, go to the directory you unpacked NVDA to, and press enter or double click on nvda.exe.

To activate your Brailliant, get to the NVDA menu by pressing NVDA+N. Select Braille settings from the Preferences menu. From the Braille display list, select HumanWare Brailliant BI/B series and press Enter. No port selection is required, you will immediately get Braille on your Brailliant display.

Command Summary for NVDA

# Using Brailliant's keys

Braille keyboard:

Use the 8-dot Perkins Braille keyboard to enter text. The 8 keys of the Braille Keyboard are located above the Braille display. Some commands are also done using Braille letters in combination with the Space bar. For example Space with the letter M to open the Menu bar.

Command Keys:

The six command keys are located on each side of the Braille cells, Dots 1-2-3 to the left and Dots 4-5-6 to the right. To do Command T, you have to press on Command keys 2-3-4-5 for the Braille letter T.

Thumb Keys:

The keys facing you are normally operated by your thumbs so we call them "Thumb Keys" to differentiate them from the main keyboard keys .Use the Thumb Keys for Braille navigation.

# Screen Reader Command summary

## JAWS command summary

Below are the command summaries for the Brailliant to be used as refreshable Braille display with JAWS. It includes JAWS commands, Windows commands, reading and navigation commands.

Your Brailliant can also be used to type text into the PC applications or to simulate the PC keyboard.

You can also define your own commands in the JAWS keyboard manager, available in the utility submenu of JAWS.

Writing with your Brailliant Braille keyboard

You can use your Brailliant's Braille keyboard to type in computer Braille with JAWS 10 and 11; US Grade 2 Braille is available in JAWS 12.

### Basic Commands

#### Braille navigation

Prior line: 	Outer Left Thumb Key Up

Move left: 	Inner Left Thumb Key Left

Move right: 	Inner Right Thumb Key Right

Next line: 	Outer Right Thumb Key Down

Move left on current line: 	Outer Left Thumb Key Up + Inner Left Thumb Key Left

Move right on current line: 	Inner Right Thumb Key Right + Outer Right Thumb Key Down

Routing cursors: 	Route Braille to position of active cursor

Active follows Braille: 	Outer Left Thumb Key Up + Outer Right Thumb Key Down

Braille follows active: 	Inner Left Thumb Key Left + Inner Right Thumb Key Right

#### Windows commands

Start Menu: 	Space with Dots 3-4

Menu Bar: 	Space with M

Application key:	Space with M and Dot 7

Minimize All Apps: 	Command D

Enter: 	Dot 8

Backspace: 	Dot 7

Escape: 	Space with E

Alt-Tab: 	Space with T

Caps lock toggle:	Space with Dot 7

Open list or combo box: 	Space with Dots 1-3-5

Close list or combo box: 	Space with Dots 2-4-6

#### Navigation commands

Up Arrow:	Space with Dot 1

Down Arrow:	Space with Dot 4

Left Arrow: 	Space with Dot 3

Right Arrow:	Space with Dot 6

Home:	Space with Dots 2-3

End:	Space with Dots 5-6

Page-Up:	Space with Dots 1-2

Page-Down: 	Space with Dots 4-5

Tab: 	Space with Dots 4-6

Shift-Tab: 	Space with K

Top of file: 	Space with L

Bottom of file: 	Space with Dots 4-5-6

Next document window: 	Space with N

Previous Document Window: 	Space with P

Close document window:	Space with Dots 2-5-6

Move Braille display to top line of screen: 	Command keys 2-3

Move Braille display to bottom line of screen:	Command keys 5-6

Read dialog box in tab order:	Command keys 2-3-4-6

#### Reading commands

Say character:	Command keys 3-6

Say prior line: 	Command key 1

Say line:	Command C

Say next line: 	Command key 3

Say word:	Command keys 2-5

Say previous word: 	Command key 2

Say next Word: 	Command key 5

Say all: 	Command keys 1-2-3-4-5-6

Toggle speech on and off: 	Command U

Select a voice profile:	Command V

#### Cursor commands

Toggle between the JAWS and PC Cursor: 	Command key 4

Route JAWS cursor to PC: 	Command I

Route Braille to active cursor: 	Command key 6

#### Braille commands

Braille toggle mode

(Line, Structured, Speech History, Attribute):   Space with Dots 2-5

Start Braille Auto Advance: 	Command R

Increase Braille Auto Advance Speed: 	Command keys 3-4-5

Decrease Braille Auto Advance Speed: 	Command keys 1-2-6

Change contracted Braille setting: 	Command G

Contracted Braille toggle in JAWS 11 or earlier: Space with G

Expand current Grade 2 word: 	Command W

Adjust JAWS options: 	Command O

Toggle between 6 and 8 dots:	Command keys 2-3-5

Adjust Braille verbosity:	Command B

#### Information commands

Keyboard Help: 	Command H

List task tray icons: 	Command keys 2-3-5-6

Hotkey Help: 	Command keys 3-5-6

JAWS window: 	Command J

Start JAWS task list: 	Command S

Say title of the active window:	Command T

Say system time:	Command Z

#### Edit commands

Cut to clipboard: 	Space with X

Copy to clipboard: 	Space with C

Paste from clipboard: 	Space with V

Delete: 	Space with D

#### Internet Explorer commands

Go back: 	Command keys 1-2-3-5-6

Go forward: 	Command keys 2-3-4-5-6

List links on a webpage: 	Command keys 3-4-6

List frames on a webpage: 	Command F

List headings on a webpage:	Command keys 2-3-6

### PC keyboard emulation for Brailliant

Entering text using your Brailliant's keyboard is very straightforward. Typing characters, changing lines, deleting characters, entering uppercase characters, and moving inside the text. JAWS simultaneously updates the Braille display to reflect what you type.

With the help of JAWS, you can enter Braille commands and control your computer using sets of keystrokes.

#### Modifier Keys

Modifier keys are used to emulate keystroke combinations that include CTRL, ALT, WINDOWS Key, SHIFT, the JAWS Key and the INSERT key. To make use of modifiers when entering text, follow these instructions:

- Press and hold SPACE with DOT 8 followed by the corresponding modifier keys.

- Once you've entered the modifier, release the keys then press the remaining portion of the keystroke. To enter CTRL+SHIFT+A, for example, you will need to press SPACE with DOTS 3-7-8, release the keys, then press A (DOT 1).

SHIFT:	SPACE with DOTS 7-8

CTRL:	SPACE with DOTS 3-8

ALT:	SPACE with DOTS 2-8

WINDOWS Key:	SPACE with DOTS 1-8

Function Keys (F1 through F12):	SPACE with DOTS 4-8

JAWS Key:	SPACE with DOTS 5-8

INSERT Key:	SPACE with DOTS 6-8

#### Function Keys

To emulate the Function keys (F1 through F12), press SPACE with DOTS 4-8 followed by the letters A through L (representing 1 through 12). If you wish to emulate the F7 key, press SPACE with DOTS 4-8, followed by G (DOTS 1-2-4-5). If you are combining a function key with another, you just need to enter the necessary modifiers while pressing down SPACE with DOTS 4-8. If you wish to emulate INSERT+F3, press SPACE with DOTS 4-5-8, followed by C (DOTS 1-4).

#### Modifier commands

The following commands can be used in combination with modifier keys:

Up Arrow:	Space with Dot 1

Down Arrow:	Space with Dot 4

Left Arrow: 	Space with Dot 3

Right Arrow:	Space with Dot 6

Home:	Space with Dots 2-3

End:	Space with Dots 5-6

Page-Up:	Space with Dots 1-2

Page-Down: 	Space with Dots 4-5

Enter: 	Dot 8

Backspace: 	Dot 7

Delete: 	Space with D

Escape: 	Space with E

Tab: 	Space with Dots 4-6

Shift-Tab: 	Space with K

Note: Modifier commands are available in the latest build of JAWS 11 and later.

## Window-Eyes command summary

Support for the Brailliant as a Braille display is integrated into Window-Eyes. Make sure to update your software to get the latest Brailliant BI driver.

Please find below a list of suggested default Braille keystrokes for the Brailliant that have been included in the Window-Eyes Braille.ini file. Feel free to alter these defaults keystrokes if they do not meet your needs.

### Window-Eyes basic commands

#### Braille navigation

Prior Braille Line: 	Thumb Key Up

Scroll Braille Left:	Thumb Key Left

Scroll Braille Right: 	Thumb Key Right

Next Braille Line: 	Thumb Key Down

Routing cursors:	Route Braille to position of active cursor

To Focus:	Command Key 6

Auto Route Cursor:	Thumb key Up with Thumb Key Down

#### Mouse HOT KEYS

Mouse Top Left:	Command Keys 1-2

Mouse Top Right:	Command Keys 4-5

Mouse Bottom Left:	Command Keys 2-3

Mouse Bottom Right:	Command Keys 5-6

Mouse To Focus:	Command I

Mouse Search:	Command F

#### Keyboard HOT KEYS

Backspace: 	Dot 7

Enter: 	Dot 8

Escape:	Space with E

Delete:	Space with D

Up-Arrow:	Space with Dot 1

Down-Arrow:	Space with Dot 4

Left Arrow:	Space with Dot 3

Right Arrow:	Space with Dot 6

Home:	Space with Dots 2-3

End:	Space with Dots 5-6

Page-Up:	Space with Dots 1-2

Page-Down:	Space with Dots 4-5

Open list or combo box (Alt-Up Arrow):	Space with O

Close list or combo box (Alt-Down Arrow):	Space with Dots 2-4-6

Top of file (Control-Home): 	Space with L

Bottom of file (Control-End): 	Space with Dots 4-5-6

Exit application (Alt-F4):	Command keys 2-5-6

Alt-Tab:	Space with T

Shift-Tab:	Space with K

Tab:	Space with Dots 4-6

Activate the current application’s menu:	Space with M

Activate the contextual menu for the

currently selected item: 	Space with M with Dot 7

Start Menu:	Space with Dots 3-4

Minimize All Apps (Windows-D):	Command D

Windows-Tab:	Command keys 1-2-5-6

Caps Lock Toggle:	Space with Dot 7

Cut to clipboard (Control-X):	Space with X

Copy to clipboard (Control-C):	Space with C

Paste from clipboard (Control-V):	Space with V

Close document window (Control-F4):	Space with Dots 2-5-6

Previous document window

(Control-Shift-Tab):	Space with P

Next document window (Control-Tab):	Space with N

#### Window-Eyes Miscellaneous hot keys

Window-Eyes menu:	Command W

Page Navigation:	Command L

Say title of the active window:	Command T

Read To End:	Command Keys 1-2-3-4-5-6

Contracted Braille Toggle:	Command G

Display mode rotor:	Space with Dots 2-5

Key describer:	Command H

Switch language:	Command V

Sys Tray:	Command keys 2-3-5-6

Time/Date:	Command Z

To Status Line:	Command S

WE/Mouse Toggle:	Command Key 4

6/8 Dots Toggle:	Command keys 2-3-5

### Modifier Keys

Modifier keys are used to emulate keystroke combinations that include CTRL, ALT, WINDOWS Key, SHIFT and the INSERT key. To make use of modifiers when entering text, follow these instructions:

- Press and hold SPACE with DOT 8 followed by the corresponding modifier keys.

- Once you've entered the modifier, release the keys then press the remaining portion of the keystroke. To enter CTRL+SHIFT+A, for example, you will need to press SPACE with DOTS 3-7-8, release the keys, then press A (DOT 1).

SHIFT:	Space with Dots 7-8

CTRL:	Space with Dots 3-8

ALT:	Space with Dots 2-8

WINDOWS Key:	Space with Dots 1-8

INSERT Key:	Space with Dots 4-8

Function Keys

To emulate the Function keys (F1 through F12), press SPACE with DOTS 6-8 with letters A through L (representing 1 through 12). If you wish to emulate the F7 key, press SPACE with DOTS 6-8, with SPACE with DOTS 1-2-4-5 6 8. You can combine function keys after modifier commands, you just need to enter the necessary modifiers before doing the function key. If you wish to emulate INSERT+F3, press SPACE with DOTS 4-8, followed by SPACE with DOTS 1-4-6-8.

Modifier commands

The following commands can be used in combination with modifier keys:

Up Arrow:	Space with Dot 1

Down Arrow:	Space with Dot 4

Left Arrow: 	Space with Dot 3

Right Arrow:	Space with Dot 6

Home:	Space with Dots 2-3

End:	Space with Dots 5-6

Page-Up:	Space with Dots 1-2

Page-Down: 	Space with Dots 4-5

Enter: 	Dot 8

Backspace: 	Dot 7

Delete: 	Space with D

Escape: 	Space with E

Tab: 	Space with Dots 4-6

Shift-Tab: 	Space with K

## Apple iOS devices Command summary

You can use your Brailliant with the following Apple iOS devices: iPod touch (3rd generation), iPhone 5, iPhone 4 and 4S, iPhone 3GS), iPod touch (4th generation).

### Basic navigation commands

Move to previous item 		Command key 1 or Space with Dot 1

Move to next item 		Command key 4 or Space with Dot 4

Pan Braille to the left			Thumb key Left or Command key 2

Pan Braille to the right		Thumb key Right or Command key 5

Double-tap the selected item			Routing cursor

Activate the Home button		Command H or Space with H

Launch the task switch 	     Command H twice quickly

Move to the first element	     Command keys 1-2-3 or Space with Dots 1-2-3

Move to the last element	     Command keys 4-5-6 or Space with Dots 4-5-6

Scroll left one page	     Command keys 2-4-6 or Space with Dots 2-4-6

Scroll right one page	     Command O or Space with O

Activate the Return key	     Space with Dot 8 or Command E

Activates a Back button if present	     Command B or Space with B

### Reading commands

Read page starting at selected item	     Command R or Space with R

Read page starting at the top		     Command W or Space with W

Scroll down one page	     Command keys 1-4-5-6 or Space with Dots 1-4-5-6

Scroll up one page 	     Command keys 3-4-5-6 or Space with Dots 3-4-5-6

Pause or Continue speech	 	Command P or Space with P

### Information commands

Go to the Status bar		Command S or Space with S

Start VoiceOver help				Command K or Space with K

Quit VoiceOver help 				Command B or Space with B

Speak page number or rows being displayed Command keys 3-4 or Space with Dots 3-4

### Rotor commands

Move to previous item using rotor setting      Command key 3 or Space with Dot 3

Move to next item using rotor setting             Command key 6 or Space with Dot 6

Select previous rotor setting                           Command keys 2-3 or Space with Dots 2-3

Select next rotor setting                                  Command keys 5-6- or Space with Dots 5-6

### Edit commands

Select text	     Command keys 2-5-6 or Space with Dots 2-5-6

Unselect text	     Command keys 2-3-5 or Space with Dots 2-3-5

Select all	     Command keys 2-3-5-6 or Space with Dots 2-3-5-6

Cut 		Command X or Space with X

Copy		Command C or Space with C

Paste 		Command V or Space with V

Activates the Delete key		Command D or Space with Dot 7

Redo 	     Command keys 2-3-4-6 or Space with Dots 2-3-4-6

Undo		Command Z or Space with Z

### Miscellaneous commands

Activate the Volume Up button	      Command keys 3-4-5 or Space with Dots 3-4-5

Activate the Volume Down button	      Command keys 1-2-6 or Space with Dots 1-2-6

Switch between 8 and 6 dot Braille 	      Command keys 2-3-6 or Space with Dots 2-3-6

Toggle speech on and off		Command M or Space with M

Toggle Screen Curtain on and off	      Command keys 1-2-3-4-5-6 or

Space with Dots 1-2-3-4-5-6

Switch between contracted and

uncontracted Braille 	      Command G or Space with G

Toggle expanded status description

when Status cells are activated                       Status Routing cursors

Activate the Tab key		Command T or Space with T

Activate the Shift with Tab keys	      Command keys 1-2-5-6 or Space with Dots 1-2-5-6

Toggle announcement history		Command N or Space with N

Activates the Eject key	     Command keys 1-4-6 or Space with Dots 1-4-6

## Mac command summary

You can use your Brailliant with Mac computers (running oSX 10.8 Mountain Lion or higher),

### Basic navigation commands

Move VoiceOver cursor up 			Thumb key Up or Command key 1

Move VoiceOver cursor down		Thumb key Down or Command key 3

Move VoiceOver cursor left			Thumb key Left

Move VoiceOver cursor right			Thumb key Right

Pan Braille to the left			Command key 2 or Space with Dot 2

Pan Braille to the right		Command key 5 or Space with Dot 5

Perform default action for current item	Routing cursor or Space with Dots 3-6

Move to the first element	     Space with Dots 1-2-3

Move to the last element	     Space with Dots 4-5-6

Scroll left one page	     Space with Dots 2-4-6

Scroll right one page	     Space with O

Return 	     Space with Dot 8 or Command E

Escape	     Command E or Space with B

Start interacting with item 	     Command key 6 or Space with Dots 2-3-6

Stop interacting with item 	     Command key 4 or Space with Dots 3-5-6

### Reading commands

Read from VoiceOver cursor 	     Space with R

Read from the beginning 		     Space with W

Scroll down one page	     Space with Dots 3-4-5-6

Scroll up one page 	     Space with Dots 1-4-5-6

Pause or Continue speech	 	Space with P

### Information commands

Start keyboard help				Space with K

Open VoiceOver Help menu 	     Space with H

Speak page number in scroll area	     Space with Dots 3-4

### Miscellaneous commands

Go to Dock 	      Command D or Space with Dots 2-5-6

Go to Menu bar	      Command M or Space with S

Go to Desktop 	      Space with Dots 2-5-6-7

Find	      Space with F

Delete	      Space with D or Space with Dot 7

Tab 		Space with T

Select previous rotor setting                           Space with Dots 2-3

Select next rotor setting                                  Space with Dots 5-6

Increase volume  	      Space with Dots 3-4-5

Decrease volume 	      Space with Dots 1-2-6

Toggle speech on and off		Space with M

Toggle Screen Curtain on and off	      Space with Dots 1-2-3-4-5-6

Switch between contracted and

uncontracted Braille 	      Command G or Space with G

Open VoiceOver Utility                                  Space with U

Item chooser                                                    Space with I

Open shortcut menu                                        Space with Dots 2-5

Toggle expanded status description                Status Routing cursors

Toggle announcement history		Command N or Space with N

Label item 		Space with Dots 1-2-3-4-6

## Using your Brailliant with System Access

Now that System Access has recognized your Brailliant, you can navigate through documents, menus, and applications with ease. In addition to using your panning bars to scroll through documents, System Access has several Braille navigation hotkeys that will help you get the most out of your display. Note that at any time, you may turn on keyboard help with Modifier+H, and you can press keys on your display to quickly learn their function.

### Braille Preferences

The Braille preferences dialog can be found by opening the System Access menu with Modifier + F, pressing the letter P for Preferences, and choosing the Braille Preferences option. Braille preferences contain two options; the first allows you to set which translation table you want to use. The default is English 8-dot Braille. The second and final option is a checkbox, allowing you to have speech while your Braille display is connected. Uncheck this box to turn off speech once your display is connected. Don't worry, once your display is disconnected, speech automatically returns. This way, you are not left with no access, or the fear your computer has crashed.

### Braille Input with System Access

System Access supports Grade II Braille input directly from the Braille keyboard of your Brailliant. Using this functionality is easy. Whenever you encounter a control which allows you to type in text, such as a search field in your browser or a Microsoft Word document, simply begin entering the text you'd like to type using your Perkins-style keyboard. This text is automatically back translated, and is entered in to the field, just as if you had typed it from your computer's keyboard. In this way, you can operate your computer completely from the Braille display, with no need to touch your computer's keyboard.

### Braille Navigation Key reference Universal Keystrokes

System Access Menu:					Command S

Menu Bar 						Space with M or Command M

Start Menu 						Space with Dots 3-4 or command keys 3-4

Recent Applications Menu or Alt+Tab 	 Space with Dots 1-2-5-6

Read Title 						Space with T	
Read status 						Space with S

Enter 							Dot 8 or Space with E

Backspace 						Dot 7 or Space with Dots 2-3

Tab 							Space with Dots 4-5 or command keys 4-6

Shift-Tab 						Space with B or Command K

Say all 							Space with Dots 1-2-3-4-5-6

Read previous line 					Space with Dot 1

Read current line 					Space with Dots 1-4

Read next line 					Space with Dot 4

Read previous word 					Space with Dot 2

Read current word 					Space with Dots 2-5

Read next word 					Space with Dot 5

Read previous character 				Space with Dot 3

Read current character 				Space with Dots 3-6

Read next character 					Space with Dot 6

Top of document 					Space with L or Command C

Bottom of document 					Space with Dots 4-5-6

Home or beginning of line 				Space with K

End or End of line 					Space with Dots 4-6

Close or Escape 					Space with Z or Command E

Move backward through the currently displayed text Thumb key Up or Command key 2

Move forward through the currently displayed text 	Thumb key Down or Command key 5

Move to the previous line 				Command key 1

Move to the next line 					Command key 4

## NVDA command summary

Scroll braille display back	left

Scroll braille display forward	right

Move braille display to previous line	up

Move braille display to next line	down

Route to braille cell	routing

Toggle braille tethered to	up+down

upArrow key	space+dot1

downArrow key	space+dot4

leftArrow key	space+dot3

rightArrow key	space+dot6

NVDA Menu	c1+c3+c4+c5 (command n)

shift+tab key	space+dot1+dot3

tab key	space+dot4+dot6

alt key	space+dot1+dot3+dot4 (space+m)

escape key	space+dot1+dot5 (space+e)

enter key	dot8

windows+d key (minimize all applications)	c1+c4+c5 (command d)

windows key	space+dot3+dot4

alt+tab key	space+dot2+dot3+dot4+dot5 (space+t)

Say all	c1+c2+c3+c4+c5+c6

# Appendix

Braille Table

Braille Alphabet

[end of document rev 5-20120412]

# Text boxes

REV 03

REV 05